## Slide 1
DCOPS • GITOPS FOR INFRASTRUCTURE OUTSIDE KUBERNETES
Certificates and domains do not stop
at the Kubernetes boundary
A control plane for visibility, ownership and safe renewal — from the domain registrar to F5, Cisco and disparate edge infrastructure.
Operational architecture and delivery proposal
Notes: [Sources]
https://github.com/microscaler/DCops

## Slide 2
THE BOUNDARY PROBLEM
cert-manager solves issuance—not the last mile
02
Microscaler • DCops
Inside Kubernetes
Secrets, Issuers and Certificate resources are native.
Renewal events can automatically update workloads.
Declarative ownership and reconciliation already exist.
CONTROL BOUNDARY
Outside Kubernetes
Certificates live in proprietary stores, profiles and trustpoints.
APIs, models, commit semantics and HA behavior differ.
A renewed Secret does not mean the service is using it.
The missing capability is controlled delivery, binding and verification.
Notes: [Sources]
https://cert-manager.io/docs/
https://github.com/microscaler/DCops

## Slide 3
WHERE WE ARE TODAY
Level 1 today: visible, unowned, and sitting on 4,000 domains
03
Microscaler • DCops
CERTIFICATES — from the discovery scan
5,368
certificates found
across the public estate
2,829
have no accountable owner
53% of everything found
1,172
issued by hand
need central management
664
expiring within 30 days
of the scan date
DOMAINS — illustrative until the registrar export is loaded
~4,000
domains in the estate
across two registrars
—
have no accountable owner
known once the export is loaded
—
registrations expiring ≤ 90 days
known once the export is loaded
Manual
Squarespace-held domains
no API — consolidate to Openprovider
How certificates are renewed today
Likely automated · 4,159
Manual, central management · 1,172
Verify · 37
Three in four certificates already renew themselves — but nobody checks that they do, one in five depends on a person remembering, and none of it matters if the domain underneath lapses.
What this means
Two inventories, both spreadsheets, neither owned. On the maturity scale this is Level 1 — the level at which outages are a matter of time.
Today: Level 1 · Initial
Source: external certificate discovery scan, 5,368 rows; domain figures are placeholders until the registrar export is loaded. Expiry counts move with the date; ownership and issuance figures are structural.

## Slide 4
THE CMMI MATURITY LADDER
Five maturity levels — for certificates and the domains under them
04
Microscaler • DCops
1
Initial
Spreadsheets and heroics. Renewals stall when one person is away.
DCOPS ADDS · CERTIFICATES
Load the scan into a single register
DCOPS ADDS · DOMAINS
Domains in a registrar login nobody shares
Today
2
Managed
Central inventory, named owners, expiry reminders.
DCOPS ADDS · CERTIFICATES
Owner assignment and 90/60/30/14/7-day alerts
DCOPS ADDS · DOMAINS
Every domain owned; registration expiry alerts
Phase 1
3
Defined
Anyone on the team can renew safely. Escalation is automatic.
DCOPS ADDS · CERTIFICATES
Escalation chain, staging-first rotation, SOP links
DCOPS ADDS · DOMAINS
Delegation and DNSSEC checked; broken chains escalate
Phase 2
4
Measured
Targets are set and tracked: no production certificate under 30 days.
DCOPS ADDS · CERTIFICATES
Live checks, Datadog dashboard and SLO monitors
DCOPS ADDS · DOMAINS
No critical domain under 90 days; delegation SLO
Phase 2
5
Optimising
Certificates renew and repair themselves. Humans only handle exceptions.
DCOPS ADDS · CERTIFICATES
cert-manager hand-off, drift detection, device delivery
DCOPS ADDS · DOMAINS
Registrar → Cloud DNS fully automated; DCops proves it
Phases 3–4
An endpoint’s level is the lower of its certificate level and its domain level — a self-renewing certificate on a lapsing domain is still Level 1.
Based on the CMMI Certificate Management Maturity Scale. Slides that deliver a capability carry a marker top-right showing the level it reaches:
Reaches Level 3 · Defined

## Slide 5
THE CONTROL PLANE
DCops extends reconciliation beyond the cluster
05
Microscaler • DCops
Git intent
Reviewed YAML
Audit trail • rollback
DCops
CRDs
Reconcilers
Policy + status
F5 adapter
iControl REST
Cisco adapter
RESTCONF • NETCONF • NX-API
Future adapters
Firewall • storage • appliances
BIG-IP
Edge
Estate
Notes: [Sources]
https://github.com/microscaler/DCops
https://github.com/microscaler/DCops/blob/main/docs/CONTROLLER_RECONCILER_ARCHITECTURE.md

## Slide 6
ONE REGISTER, NO DUPLICATION
cert-manager issues certificates. DCops keeps the register.
06
Microscaler • DCops
cert-manager — already in place
Issues and renews certificates
Public and internal, on a schedule, with no human in the loop
Holds the private keys
Securely, inside Kubernetes
Reports its own status
Ready or not, when the next renewal is due
Stays the only issuer
DCops never becomes a certificate authority
DCops register — new
Who owns every certificate — and its domain
One owner, inherited from the domain down to each certificate
Where it is used
Including sites, devices and domains cert-manager cannot see
What the live site really presents
Checked directly, not assumed from a renewal
Whether it meets policy
Approved issuer, valid chain, more than 30 days left
Reaches Level 2 · Managed
DCops records, verifies and escalates. When a manually-managed certificate can be automated, DCops hands it to cert-manager — it never re-implements it.

## Slide 7
THE FOUNDATION UNDERNEATH
A certificate is only as safe as the domain it lives on
07
Microscaler • DCops
LAYER
WHO KEEPS IT ALIVE
WHAT DCOPS CHECKS
Certificate
Issued by cert-manager or a CA; renewed on a schedule
Expiry · issuer · chain · what the live site presents
Delegation & DNS
Registry points the domain at Cloudflare or Cloud DNS; records there point at the service
Name servers match at every hop · DNSSEC chain valid · record resolves
Domain registration
Held at the registrar (Openprovider / Squarespace); renewed yearly by a person or auto-renew
Registration expiry · lock status · registrant contact still employed
▲ Each layer depends on the one below it. A failure lower down takes the site offline no matter how good the certificate is.
One owner, inherited downwards
Assign the owner of example.com once and every certificate under it is owned. Most of the 2,829 unowned certificates are unowned because their domain is.
Two registers, one wizard, no writes
The registrar export loads exactly like the certificate scan. DCops records and verifies domains; it never changes registrar or DNS settings.
Reaches Level 2 · Managed
Your certificate is useless if someone forgets to renew the domain, or its delegation lapses or is misconfigured.

## Slide 8
FROM SPREADSHEET TO LIVING REGISTER
Operations loads the scan in the DCops UI — no engineers, no YAML
08
Microscaler • DCops
1
Drop the file
Upload the certificate scan — or the registrar’s domain export — exactly as produced
2
Review the changes
New, changed, unchanged and disappeared records, side by side
3
Confirm
One click. The register updates and the import is logged
4
Assign owners
Work through the unowned list; every assignment is recorded
Safe to repeat
Loading the same file twice changes nothing. Loading next month’s scan changes only what moved.
Owners are never overwritten
A re-import can update expiry dates and issuers; it cannot touch who is responsible.
Every import is on record
Who loaded it, when, and exactly what changed — the audit trail a Level 2 review asks for.
Reaches Level 2 · Managed
One wizard, two registers. Records that vanish from a scan are flagged, never deleted — removal is always a deliberate, recorded decision.

## Slide 9
DCOPS DASHBOARD
Every certificate and domain becomes an owned operational object
09
Microscaler • DCops
DCops / Certificates Domains
Last check 32s ago
Search… Bucket: All Owner: All State: Attention required
Import scan
HOSTNAME
DOMAIN
ISSUER
EXPIRES
STATE
OWNER
api.example.com
example.com
Let’s Encrypt
89 days
Healthy
Platform
shop.example.co.za
example.co.za
DigiCert · manual
6 days
Renewal due
Commerce
mgmt.example.net
example.net
Internal CA
41 days
Drift found
Network
portal.example.org
example.org
Let’s Encrypt
52 days
Domain expires in 12 days
Unowned
SELECT A ROW TO VIEW
Observed vs expected • delegation chain • event history • planned action • owner
Reaches Level 2 · Managed
Notes: [Sources]
https://github.com/microscaler/DCops

## Slide 10
PROACTIVE COMMUNICATION
Alerts follow the lifecycle — and distinguish action from assurance
10
Microscaler • DCops
Renewal due
90 / 60 / 30 / 14 / 7 days
Owner reminder with target, expiry, policy and planned renewal window.
Microsoft Teams + Email
Domain expiring
90 / 60 / 30 days
Registrant owner reminder with registrar, auto-renew status and every certificate that would go down with it.
Microsoft Teams + Email
Delegation broken / DNSSEC invalid
Immediately — an outage in progress
Owner and platform team: which hop disagrees (registry, Cloudflare, Cloud DNS) and the Git change that fixes it.
Microsoft Teams + Email
Renewal succeeded
After live verification
Confirmation with new fingerprint, active binding and evidence — checked at the edge and, behind a proxy, at the origin.
Microsoft Teams + Email
Renewal failed
Immediately; escalate on retry
Teams incident card and email with failure stage, safe state, retry and runbook.
Microsoft Teams + Email
Success is announced only after device readback and live TLS verification — at the edge and at the origin. Delegation and expiry alerts never wait for a scan.
Reaches Level 3 · Defined
Notes: [Sources]
https://learn.microsoft.com/en-us/microsoftteams/platform/webhooks-and-connectors/how-to/connectors-using
https://docs.datadoghq.com/monitors/notify/

## Slide 11
OPERATIONS DASHBOARD
Datadog gives Operations one fleet-level certificate view
11
Microscaler • DCops
Certificate posture • Global estate
SITE: ALL VENDOR: ALL ENV: PROD
1,284
managed
37
≤ 30 days
8
renewal failed
99.2%
verified
EXPIRY HORIZON
> 60 days
1040
31–60
207
8–30
29
≤ 7
8
TOP EXCEPTIONS
edge-sofia-12
F5
renewal failed
rtr-bansko-03
IOS XE
expires in 6 days
nx-dc2-01
NX-OS
verification drift
Illustrative dashboard layout—metrics and thresholds are configurable.
Reaches Level 4 · Measured
Notes: [Sources]
https://docs.datadoghq.com/dashboards/
https://docs.datadoghq.com/monitors/

## Slide 12
DATADOG INTEGRATION
Built the Datadog way: a packaged integration, not a custom script
12
Microscaler • DCops
DCops
Checks every certificate and domain on a schedule and publishes standard health figures
Datadog integration
Built to Datadog’s own integration standard — the same pattern as their cert-manager integration
Operations dashboard
Fleet view by site, vendor, owner and expiry horizon — the previous slide
Teams + email
Ready-made monitors route each alert to the accountable owner
Six monitors ship with the integration
Expiring certificate
Any production certificate under 30 days — the Level 4 target
Expiring domain
Any critical domain registration under 90 days, or auto-renew off
Drift
The live site is not presenting the certificate we issued — edge or origin
Delegation / DNSSEC
A hop in the chain disagrees, or validation fails — an outage in progress
Unowned
A critical certificate or domain with nobody accountable
Stale inventory
No certificate scan or registrar export loaded for more than a week
Reaches Level 4 · Measured
“Renewal succeeded” is only ever sent after DCops has checked the live site. Datadog carries the message; DCops supplies the proof.

## Slide 13
WHAT LEADERSHIP WILL SEE
Five numbers that tell you whether the estate is getting safer
13
Microscaler • DCops
Owner coverage · target
100%
of critical certificates and domains with a named, accountable owner
Today: 47% of certificates
Renewal headroom · target
100%
of production certificates with more than 30 days left
The Level 4 service objective
Registration headroom · target
100%
of critical domains with more than 90 days before renewal
Illustrative until the export is loaded
Automation coverage · trend
↑
share of certificates that renew without a person involved
Today: about 77%, unverified
Time to rotate · trend
↓
hours from alert to a verified new certificate on the live site
Justifies each automation step
Reaches Level 4 · Measured
Maturity is measured, not asserted
Every endpoint is scored on the five-level scale from facts DCops can see: is it owned, is it checked, does it meet the target, does it renew itself — and the score is the lower of its certificate and its domain.
The estate’s level is the level of its weakest critical endpoint, so one unowned domain keeps the whole estate at Level 1.
Endpoints by level — illustrative
L1
L2
L3
L4
L5

## Slide 14
WHY THIS IS HARD
One certificate lifecycle meets many incompatible control planes
14
Microscaler • DCops
F5 BIG-IP
iControl REST
SSL profiles • HA sync
save config
PERSISTENCE
Cisco IOS XE
RESTCONF / NETCONF
trustpoints • YANG revisions
commit / write memory
PERSISTENCE
Cisco IOS XR
NETCONF / gNMI
CEPKI • release variance
candidate / running
PERSISTENCE
Cisco NX-OS
NX-API / YANG
feature-dependent PKI
checkpoint / copy run start
PERSISTENCE
The adapter must understand the device - not merely copy PEM files.
Notes: [Sources]
https://clouddocs.f5.com/api/icontrol-rest/APIRef.html
https://developer.cisco.com/site/networking/
https://developer.cisco.com/site/nx-os/

## Slide 15
OPERATIONAL RISK
The most dangerous failures look successful at first
15
Microscaler • DCops
01
Renewed, not bound
The new certificate reaches the device but the active profile still references the old object.
02
Applied, not persisted
Traffic works until reboot because running configuration was never saved.
03
Updated, not synchronized
One member of an HA pair is correct while its peer remains stale.
04
Installed, not trusted
The leaf is present but the intermediate chain or trust anchor is wrong.
05
Automated, not verified
The API returns success; the live endpoint still presents the wrong fingerprint.
06
Alerted, not owned
Expiry alarms exist but nobody has accountable remediation ownership.
07
Renewed, not resolvable
The certificate is perfect; the domain lapsed at the registrar or its delegation points at nothing. The site is down anyway.
08
Verified at the edge, not the origin
Behind a proxy the public endpoint presents the proxy’s certificate; ours can expire on the server with nobody noticing.
Notes: [Sources]
https://clouddocs.f5.com/api/icontrol-rest/APIRef_tm_ltm_profile_client-ssl.html
https://www.cisco.com/c/en/us/td/docs/ios-xml/ios/prog/configuration/179/b_179_programmability_cg/m_178_prog_restconf.html

## Slide 16
CERTIFICATE LIFECYCLE
Every renewal becomes a controlled, observable transaction
16
Microscaler • DCops
1
Detect
Secret changes or renewal window opens
2
Validate
Key match, chain, SANs and policy
3
Stage
Create immutable fingerprinted objects
4
Activate
Switch binding using device semantics
5
Verify
Read back state; probe live TLS at the edge and the origin
6
Retain
Keep last-known-good, then clean safely
Any failed verification triggers rollback and an actionable alert.
Reaches Level 5 · Optimising
Notes: [Sources]
https://github.com/microscaler/DCops
https://cert-manager.io/docs/

## Slide 17
ADAPTER STRATEGY
A common contract prevents vendor logic leaking into operations
17
Microscaler • DCops
Capability discovery
Version • platform • writable models • HA role
Inspect
Fingerprint • expiry • binding • persistence
Stage
Upload/import without touching live traffic
Activate
Vendor-specific atomic switch or guarded command set
Verify
API readback plus endpoint TLS probe
Rollback & cleanup
Restore last-known-good; delete only unreferenced objects
Unsupported is a valid result. Silent fallback is not.
Reaches Level 5 · Optimising
Notes: [Sources]
https://github.com/microscaler/DCops
https://github.com/YangModels/yang

## Slide 18
SECURITY & GOVERNANCE
Automation must reduce certificate risk - not redistribute it
18
Microscaler • DCops
Keys
Kubernetes Secrets; memory only; never status or logs
Identity
Per-controller device accounts and least privilege
Trust
Pinned management CA; no production TLS bypass
Idempotency
Immutable names derived from certificate fingerprint
Concurrency
One lock per target and binding
Rollback
Retain last-known-good until verification settles
Deletion
Finalizer plus orphan policy; never delete live references
Evidence
Events, fingerprints, API receipts and external probes
Notes: [Sources]
https://kubernetes.io/docs/concepts/configuration/secret/
https://github.com/microscaler/DCops

## Slide 19
WHY DCOPS
GitOps supplies the missing operating discipline
19
Microscaler • DCops
Traditional device automation
DCops reconciliation
Run a script when someone remembers
Continuously converge desired and observed state
Success means the command returned zero
Success means the live service presents the intended certificate
Changes live in tickets and operator memory
Intent, approvals and rollback live in Git
Vendor workflows leak into every runbook
Adapters absorb vendor-specific semantics
Drift is discovered during incidents
Drift becomes visible and actionable
Credentials and logs vary by script
One security, event and status model
Git declares intent. DCops makes it true.
Notes: [Sources]
https://opengitops.dev/
https://github.com/microscaler/DCops

## Slide 20
WHERE DCOPS WRITES — AND WHERE IT ONLY WATCHES
DCops changes devices; Git changes domains, and DCops proves it
20
Microscaler • DCops
Devices — DCops writes
F5, Cisco and future adapters
Stage, activate, verify and roll back certificates on the device
Reviewed intent in Git
DCops converges the device to what Git declares
Verification before success
Readback plus live TLS probe before anyone is told it worked
Needs device credentials
Least-privilege, per-controller accounts — the only credentials that can change anything
This is the hard, valuable part: Phases 3–4.
Domains & DNS — DCops only watches
Registrar, Cloudflare, Google Cloud DNS
Changed by the client’s Terraform and ExternalDNS pipelines, never by DCops
DCops reads and resolves
Registrar records, DNS zones and live resolution from public resolvers
DCops proves the chain
Registration current, every hop agrees, DNSSEC validates, records resolve
The fix is a reviewed change
A broken delegation raises an alert that links to the Git change that repairs it
This is why the domain register is cheap: Phase 1, no adapters.
Precondition: the registrar must have an API. Openprovider does. Squarespace-held domains can only be changed by hand — consolidate them first (Phase 0).

## Slide 21
DELIVERY ROADMAP
Start with both registers, prove each level, then expand by platform
21
Microscaler • DCops
0
Foundation
Approve scope; consolidate registrars onto one with an API; build the register and reporting foundations
1
Register
Load the scan and the registrar export, assign owners, alert on certificate and domain expiry — Level 2
2
Verification
Live checks including delegation and DNSSEC, Datadog dashboard and monitors, Teams and email — Levels 3–4
3
Automation
Hand cloud certificates to cert-manager; detect drift — Level 5 for cloud
4
Delivery
F5 pilot with verified rollback, then Cisco — Level 5 for legacy
Each phase lifts a measurable maturity level before the next begins.
Notes: [Sources]
https://github.com/microscaler/DCops

## Slide 22
THE DECISION
Make certificate and domain state
a continuously reconciled fact
Approve the certificate and domain registers, the Datadog integration and the F5 pilot. Measured against the CMMI scale, this takes a 5,368-row spreadsheet and 4,000 domains from Level 1 to an owned, measured estate — and opens a safe path from Kubernetes-issued certificates to the infrastructure that actually serves traffic.
Next milestone
Scan and registrar export loaded, every critical certificate and domain owned, and the Operations dashboard live in Datadog.
Microscaler • DCops
Notes: [Sources]
https://github.com/microscaler/DCops